Combi - Motor Inverter Ampseal 35 Pinout

1 - GND

2 – GND

3 - SIGNAL ON. 0V OFF. 12V ON. - Cruise Control

4 – SIGNAL START. 0V OFF. 12V ON.

5 – SIGNAL BRAKE. 0V OFF. 12V ON.

6 – THROTTLE INPUT. 0 TO 5V INPUT.

7 – SPARE ANALOG INPUT – regen pot

8 – SIGNAL MOTOR PROTECTION SWITCH

9 – SIGNAL FORWARD

10 – SIGNAL REVERSE

11 – SIGNAL BMS

12 – MAIN CONTACTOR OUTPUT. NPN OPEN COLLECTOR.

13 – PRECHARGE RELAY OUTPUT. NPN OPEN COLLECTOR.

14 – ERROR OUTPUT. NPN OPEN COLLECTOR.

15 – N/C

16 – OVER TEMP OUTPUT. NPN OPEN COLLECTOR.

17 – SIGNAL EMERGENCY STOP SWITCH.

18 – TEMPERATURE GAUGE DRIVER. PWM. Also rpm output

19 – ENCODER NPUT. 5V PULLUP FITTED. FOR USE WITH NPN OPEN COLLECTOR ENCODER.

20 – 5V OUTPUT.

21 – MOTOR TEMP SENSOR NEGATIVE.

22 – MOTOR TEMP SENSOR POSITIVE.

23 – 12V DC MAIN INPUT.

24 – 5V OUTPUT.

25 – GND

26 – RPM OUTPUT. TACHOMETER DRIVER. VARIABLE FREQUENCY. NOT YET IMPLIMENTED. 12V SQUARE WAVE.

31 – FTCAN High

32 – FTCAN Low

33 – CAN High

34 – CAN Low

35 – GND